## Slide 1: PID GAIN OPTIMIZATION
INTERNAL COMBUSTION ENGINE AT
IDLE SPEED
RAJDEEP arora & Yi cheng yeh

## Slide 2: oVERVIEW
Manual Tuning
Fmincon Optimization
Particle Swarm Optimization – Introduction
Particle Swarm Optimization - Results
Results discussion

## Slide 3
Open loop
Throttle angle
Engine speed
Signal Statistics
ENGINE SPEED
Max : 1590 RPM
Min : 100 RPM
Mean : 766.8 RPM
Signal Statistics
ThROTTLE ANGLE
Max : 9.8◦
Min : 9.8◦
Mean : 9.8◦

## Slide 4
Close loop {kp: 0.1, ki: 0.005, Kd: 1}
Throttle angle
Engine speed
Signal Statistics
ENGINE SPEED
Max : 964.5 RPM
Min : 636 RPM
Mean : 798.8 RPM
Signal Statistics
ThROTTLE ANGLE
Max : 14.7◦
Min : 6.835◦
Mean : 7.9◦

## Slide 5
Close loop {kp: 0.2, ki: 0.005, Kd: 2}
Throttle angle
Engine speed
Signal Statistics
ENGINE SPEED
Max : 936.9 RPM
Min : 677.8 RPM
Mean : 799.2 RPM
Signal Statistics
ThROTTLE ANGLE
Max : 16.72◦
Min : 6◦
Mean : 11.73◦

## Slide 6
Close loop {kp: 0.225, ki: 0.01, Kd: 4.25}
Throttle angle
Engine speed
Signal Statistics
ENGINE SPEED
Max : 922.2 RPM
Min : 707.4 RPM
Mean : 800.6 RPM
Signal Statistics
ThROTTLE ANGLE
Max : 20◦
Min : 6◦
Mean : 11.71◦

## Slide 7
Fmincon
Non-linear optimization

## Slide 8: FMINCON : Initial gain {kp: 0.01, ki: 0.001, Kd: 1}
Signal Statistics
ENGINE SPEED
Max : 1017 RPM
Min : 556 RPM
Mean : 796 RPM
OBJECTIVE
FUNCTION
FMINCON : FINAL gain {kp: 0.01, ki: 0.001, Kd: 0.89 }
Absolute Error
Signal Statistics
ThROTTLE ANGLE
Max : 13.37 ◦
Min : 7.37◦
Mean : 11.7◦
Metrics = ∑ Errors
1.17e+07

## Slide 9: FMINCON : Initial gain {kp: 0.01, ki: 0.001, Kd: 1}
Signal Statistics
ENGINE SPEED
Max : 1014 RPM
Min : 561 RPM
Mean : 794 RPM
OBJECTIVE
FUNCTION
FMINCON : FINAL gain {kp: 0.01, ki: 0.001, Kd: 1.0}
Norm Square Error
Signal Statistics
ThROTTLE ANGLE
Max : 13.37 ◦
Min : 7.37◦
Mean : 11.7◦
Metrics = ∑ Errors
1.24e+07

## Slide 10: FMINCON : Initial gain {kp: 0.01, ki: 0.001, Kd: 1}
Signal Statistics
ENGINE SPEED
Max : 1014 RPM
Min : 561 RPM
Mean : 791 RPM
OBJECTIVE
FUNCTION
FMINCON : FINAL gain {kp: 0.01, ki: 0.001, Kd: 1.0}
T * Norm Square
Signal Statistics
ThROTTLE ANGLE
Max : 13.37 ◦
Min : 7.37◦
Mean : 11.6◦
Metrics = ∑ Errors
1.24e+07

## Slide 11: FMINCON : Initial gain {kp: 0.225, ki: 0.01, Kd: 4.25}
Signal Statistics
ENGINE SPEED
Max : 921 RPM
Min : 706 RPM
Mean : 800 RPM
OBJECTIVE
FUNCTION
FMINCON : FINAL gain {kp: 0.27, ki: 0.01, Kd: 4.09}
Absolute Error
Signal Statistics
ThROTTLE ANGLE
Max : 20◦
Min : 6◦
Mean : 14◦
Metrics = ∑ Errors
2.70e+06

## Slide 12: FMINCON : Initial gain {kp: 0.225, ki: 0.01, Kd: 4.25}
Signal Statistics
ENGINE SPEED
Max : 920 RPM
Min : 709 RPM
Mean : 800 RPM
OBJECTIVE
FUNCTION
FMINCON : FINAL gain {kp: 0.2757, ki: 0.0076, Kd: 4.3738}
Norm Square Error
Signal Statistics
ThROTTLE ANGLE
Max : 20◦
Min : 6◦
Mean : 14◦
Metrics = ∑ Errors
2.85e+06

## Slide 13: FMINCON : Initial gain {kp: 0.225, ki: 0.01, Kd: 4.25}
Signal Statistics
ENGINE SPEED
Max : 925 RPM
Min : 707 RPM
Mean : 800 RPM
OBJECTIVE
FUNCTION
FMINCON : FINAL gain {kp: 0.2058, ki: 0.0075, Kd: 4.2415}
T * Norm Square
Signal Statistics
ThROTTLE ANGLE
Max : 20◦
Min : 6◦
Mean : 11.7◦
Metrics = ∑ Errors
2.83e+06

## Slide 14
Particle Swarm Optimization

## Slide 15: PARTICLE SWARM OPTIMIZATION
Particle Direction
Global Minima
(Social)
Local Minima (Cognitive)
Particle’s Randomness in Velocity
Each Particle keeps track of swarm’s best so far solution
Each Particle keeps track of its own best so far position
PD
Global
L-Min
0
1

## Slide 16: PSO….
Social = 0, Cognitive = 0.8
Social = 0.8, cognitive = 0
Randomness = 0

## Slide 17: PSO….
Randomness = 0
Randomness <> 0
Cognitive = 0.6, social = 0.3

## Slide 18: Initial gain {kp: 0.01, ki: 0.001, Kd: 1} HYPER-PARAMETERS {w = 0.2, c1 = 0.3, c2 = 0.6}
Signal Statistics
ENGINE SPEED
Max : 1001 RPM
Min : 586 RPM
Mean : 797 RPM
OBJECTIVE
FUNCTION
FINAL gain {kp: 0.229, ki: 0.002, Kd: 1.0013}
Absolute Error
Signal Statistics
ThROTTLE ANGLE
Max : 13.67◦
Min : 7.05◦
Mean : 11.7◦
Metrics = ∑ Errors
1.0e+07

## Slide 19: Initial gain {kp: 0.01, ki: 0.001, Kd: 1} HYPER-PARAMETERS {w = 0.2, c1 = 0.3, c2 = 0.6}
Signal Statistics
ENGINE SPEED
Max : 987 RPM
Min : 614 RPM
Mean : 795 RPM
OBJECTIVE
FUNCTION
FINAL gain {kp: 0.06, ki: 0.0015, Kd: 1.0}
Norm Square Error
Signal Statistics
ThROTTLE ANGLE
Max : 14◦
Min : 6.9◦
Mean : 11.7◦
Metrics = ∑ Errors
1.0e+09

## Slide 20: Initial gain {kp: 0.01, ki: 0.001, Kd: 1} HYPER-PARAMETERS {w = 0.2, c1 = 0.3, c2 = 0.6}
Signal Statistics
ENGINE SPEED
Max : 1012 RPM
Min : 565 RPM
Mean : 795 RPM
OBJECTIVE
FUNCTION
FINAL gain {kp: 0.0096, ki: 0.0014, Kd: 1.0}
T * Norm Square
Signal Statistics
ThROTTLE ANGLE
Max : 13.53◦
Min : 7.1◦
Mean : 11.7◦
Metrics = ∑ Errors
1.0e+10

## Slide 21: Initial gain {kp: 0.225, ki: 0.01, Kd: 4.25} HYPER-PARAMETERS {w = 0.2, c1 = 0.3, c2 = 0.6}
Signal Statistics
ENGINE SPEED
Max : 921 RPM
Min : 707 RPM
Mean : 800 RPM
OBJECTIVE
FUNCTION
FINAL gain {kp: 0.024, ki: 0.0096, Kd: 4.2525}
Absolute Error
Signal Statistics
ThROTTLE ANGLE
Max : 20◦
Min : 6◦
Mean : 14◦
Metrics = ∑ Errors
1.0e+06

## Slide 22: Initial gain {kp: 0.225, ki: 0.01, Kd: 4.25} HYPER-PARAMETERS {w = 0.2, c1 = 0.3, c2 = 0.6}
Signal Statistics
ENGINE SPEED
Max : 920 RPM
Min : 707 RPM
Mean : 800 RPM
OBJECTIVE
FUNCTION
FINAL gain {kp: 0.223, ki: 0.0077, Kd: 4.2594}
Norm Square Error
Signal Statistics
ThROTTLE ANGLE
Max : 20◦
Min : 6◦
Mean : 11.7◦
Metrics = ∑ Errors
1.0e+07

## Slide 23: Initial gain {kp: 0.225, ki: 0.01, Kd: 4.25} HYPER-PARAMETERS {w = 0.2, c1 = 0.3, c2 = 0.6}
Signal Statistics
ENGINE SPEED
Max : 920 RPM
Min : 707 RPM
Mean : 800 RPM
OBJECTIVE
FUNCTION
FINAL gain {kp: 0.2244, ki: 0.0060, Kd: 4.2431}
T * Norm Square
Signal Statistics
ThROTTLE ANGLE
Max : 20◦
Min : 6◦
Mean : 11.7◦
Metrics = ∑ Errors
1.0e+08

## Slide 24: PSO….
Hyperparameters
{w = 0.4, c1 = 0.6, c2 = 0.3}
Hyperparameters
{w = 0.2, c1 = 0.3, c2 = 0.15}
Metrics = ∑ Errors
1.0e+08
1.0e+07
COSTS
OBJECTIVE
FUNCTION
T * Norm Square

## Slide 25: FUTURE SCOPE
There is a scope of hyper-parameter (randomness, cognitive and social) tuning of Particle Swarm Optimization using another non-linear optimization algorithms
Identify which objective function to apply based on use cases
Settling Time should also be taken into consideration for model performance evaluation
PID Gain Optimization for IC Engine